## Slide 1: Multi-Agent Decision Support System for Space Mission Operations
Master’s Degree in AI & Robotics Antonio Lissa Lattanzio (2154208)
Academic Year 2025/2026
Advisor
Prof. Danilo Comminiello
Co-Advisor
Daniele Baldassini

## Slide 2
01
03
Operative Context
Proposed System
Conclusions, Limitations and Future Work
Foundation and Existing Approaches
04
05
02
System Evaluation
Presentation Outline

## Slide 3
Ground Segment Organization
Satellite Control Center: spacecraft monitoring and command execution.
Mission Planning Center: planning of operational activities and mission tasks.
TT&C: telemetry acquisition, spacecraft tracking and command uplink
Flight Dynamics: orbit determination, maneuver planning and analysis.
...
Although each system performs a well-defined function, mission operations emerge from their continuous interaction.
Mission Manager: The person responsible for supervising the overall execution and state of the mission.

## Slide 4
Mission Manager’s Role & Challenges
Situational Awareness
Supervising mission execution and anomaly responses.
Operational events evaluation.
Response coordination of different teams.
Support of decision-making during nominal and contingency scenarios.
Information Fragmentation
Integrate informations from multiple sources.
The evidence are heterogeneous, asynchronous, incomplete or even conflicting.
Rapid identification of important informations and their implications.

## Slide 5
Research Questions
01
Autonomous LLM Capabilities
To what extent can Large Language Models autonomously conduct cross-domain reasoning while maintaining accuracy and robustness?
02
Retrieval Pipeline
Can a specialized agentic retrieval pipeline improve the quality of the decision support task compared to a general purpose LLM?

## Slide 6
Foundation and Existing Approaches
01
03
Operative Context
Proposed System
Conclusions, Limitations and Future Work
Foundation and Existing Approaches
04
05
02
System Evaluation
03
04
05

## Slide 7
Current SOTA for DSS in space missions
Kaisheng et al. | Autonomous EVA [2026]
Earth-independent DSS for deep space operations.
Agentic AI integrating fine-tuned LLMs, RAG and physics based simulations.
Maranto et al. | LLMSAT [2024]
High-level mission planning and decision support for space exploration.
Hierarchical LLM integrating RAG, flight-software interfaces and simulation based planning.
Research GAP
Existing solutions remain domain specific and prototype oriented, with limited integration of heterogeneous operational data and knowledge.

## Slide 8
Proposed system
01
03
Operative Context
Proposed System
Conclusions, Limitations and Future Work
Foundation and Existing Approaches
04
05
02
System Evaluation

## Slide 9: FUNES System
The FUNES system is designed to be an intermediate layer between existing mission operational systems and human operators.
It does not replace mission operators, it supports human decision-making by improving situational awareness, reducing information fragmentation, and providing recommendations.
Custom RAG system
CI-2 AI Module
CI-1 Data Processing
CI-5 Storage
CI-3 UI
CI-4 Config & Model Management
AI config
SM config
Config settings
DPM config
Queries
Inference results
Inference results
RAG data
Operators
interactions
Normalized
data
External data sources

## Slide 10: FUNES System – PoC Chat capability

## Slide 11: FUNES PoC - AI Module
Multi-Agent Graph-Based Architecture (LangGraph): The system decomposes the decision-making process into specialized LLM components, coordinated through a shared execution state.
Role Specialization and Separation: Agents are divided into core-orchestration roles and tool-support agents, ensuring evidence-grounded assessments with structured JSON outputs.
Every LLM is constrained to follow a specific JSON answer model.

## Slide 12
Introduction
Foundation and Existing Approaches
System Evaluation
Conclusions, Limitations and Future Work
Foundation and Existing Approaches
System Evaluation
01
03
Proposed System
04
05
02

## Slide 13: Proposed Scenario
Planning: 32 hrs of planning data for each satellite
Network State:
      GS-01 is degraded: ANT-02 offline, ANT-03 exhibits latency and packet loss.
      GS-01 ↔ GS-02 degraded
32 operational tickets:
3 are related to the malfunctions
1 is for preventive maintenance on GS-02/ANT-02 that requires replanning
1 is about an urgent acquisition that requires replanning of activities
Knowledge base: 20 documents in the RAG system

## Slide 14
Evaluation Benchmark
10 Easy
6 Medium
4 Hard

## Slide 15
Evaluation Methodology
FUNES
Query
Retrieved useful context
Llama 3.3 70B
Query
Full context of 24K tokens
VS
LLM as a judge
Query
Scenario description
Evaluation instructions
Answers
Answer correctness
Correctly addressing of the question given the operational knowledge.
Noise Filtering
Distinguish relevant from unrelated informations.
Anomaly Identification
Identify and characterize operational anomalies.
DSS Role Adherence
Correct answer behaviour (evidence-based situational awareness etc…).
Evidence Correlation
Establish correct correlations between evidences from different sources.
Op. Reccom. Quality
Quality of reccomendations when actions are required.

## Slide 16
Evaluation Methodology – Scoring Instructions
Score 0 - Incorrect
Assigned for material, factual or operational errors affecting the criterion (e.g., false statements, operational contradictions, incorrect correlations, or incompatible recommendations).
Minor imprecisions or isolated omissions were not sufficient to warrant a score of 0.
Score 1 - Partially correct
Assigned when the answer was substantially correct but had significant limitations... (e.g., omission of relevant info, partial correlations, generic recommendations).
It indicated the answer was useful but did not fully meet the requirements.
Score 2 - Fully correct
Assigned when the answer fully satisfied the criterion... by providing all requested info, correctly incorporating operational evidence, establishing supported correlations, and giving appropriate, evidence-consistent recommendations.
The judge is not blindly assigning a score!

## Slide 17
Evaluation Results
Chart: Results by Task Complexity (%)
| Easy | Medium | Hard
FUNES | 96 | 87 | 86
Llama | 46 | 72 | 74
Chart: Overall Results (%)
| Overall result
FUNES | 90
Llama | 63

## Slide 18
Evaluation Results – Some cases
Q5: How many passes does satellite SAT-02 have on 2026-05-26 on GS-02?
Model | AC | NF | Total
Llama | 0 | 0 | 0/4
FUNES | 2 | 2 | 4/4
Q19: Identify risks for planned activities on 2026-05-26 and report the affected activities with their corresponding datetime.
Model | AC | AI | EC | NF | DSS | Total
Llama | 2 | 2 | 2 | 2 | 2 | 10/10
FUNES | 1 | 2 | 1 | 1 | 2 | 7/10

## Slide 19
Conclusions, Limitations and Future Work
01
03
Operative Context
Proposed System
Conclusions, Limitations and Future Work
Foundation and Existing Approaches
04
05
02
System Evaluation

## Slide 20
Conclusions
The observations must be interpreted within the limits of the proposed benchmark.
They do not establish a general rule for task-dependent performances.
The results indicate that the benefits of FUNES depend on the type of reasoning required by the task.
The system is effective at limiting the required information but this does not always translate to the ability of fully answering the query.
The advantages diminishes on complex questions that require more informations and context.

## Slide 21
Limitations
Benchmark Scope & sample size
The evaluation is limited to 20 questions in a single scenario, limiting statistical robustness.
Single baseline
The evaluation compare FUNES against a single model, general superiority over other LLMs must be studied.
API Constraint
Groq API rate/token limits restricted repeated runs under identical experimental conditions.
Evaluation and Metrics Constraints
The LLM as a judge and unweighted criteria may introduce bias and ignore criticality of specific metrics.
Ablation Study
The system is evaluated as a complete architecture, preventing isolation of individual contributions.

## Slide 22
Future Work
Synthesis & Validation
Extend the critic agent to check the synthesizer answer.
LLM Efficiency
Evaluate FUNES across diverse model sizes. (The orchestration can compensate smaller models)
Benchmark Scaling
Expand the benchmark with larger datasets, complex temporal dependencies and ambiguities
Human in the Loop
Evaluate real-world usability, operational trust and impact metrics like time-to-decision.
Evidence Grounding
Introduce evidence graphs for full e2e treceability of the whole system reasoning steps.

## Slide 23
Thank you for your Attention
Any Questions?